PRESS RELEASE	Contact: 	Simone Hebel, Market Manager, Europe
		ITW Test & Measurement GmbH
		In der Steele 2
		D-40599 Düsseldorf/Germany
		Phone +49-(0)211-9741027
		Email: simone.hebel@buehler.com

Buehler at Control 2015:

PlanarMet 300 – New planar grinder accelerates sample preparation in metallography

The new Buehler PlanarMet 300 bench-top planar grinding machine utilizes a fixed abrasive stone for rapid sample grinding, and accommodates up to 10 samples at a time in a central-force specimen holder. 
© Buehler – ITW Test & Measurement GmbH

Dear editors, please download this Buehler press release including text and ready-to-print image file from: www.konsens.de/buehler.html

Buehler at Control 2015:

PlanarMet 300 – New planar grinder accelerates sample preparation in metallography

Düsseldorf/Germany, March 2015 – PlanarMet 300 is a new bench-top planar grinder from Buehler – ITW Test & Measurement GmbH which provides rapid, highly accurate and convenient sample preparation in metallography. Using a fixed 305 mm (12 in) grinding stone in conjunction with a high-performance motor PlanarMet 300 is designed to remove up to 0.6 mm of material per minute – up to ten times faster than grinding with SiC paper. The central-force specimen holder, accommodating up to 10 samples at a time, enables three to four grinding stages to be combined into a single step, whereby the amount of material to be removed can be programmed accurately in increments of 0.1 mm. The time and cost saving PlanarMet 300 system therefore offers all the power of a large, floor-standing model in a space-saving, compact bench-top design.

For highly accurate material removal, the grinder offers either a timed-cycle or a controlled material depth mode, with adjustable powerhead speed and direction of rotation. Sample deformation is kept to a minimum by an integral cooling water inlet, combined with a unique water manifold, which ensures adequate cooling even under extremely aggressive grinding conditions. The self-calibrating auto-dressing system with adjustable dressing frequency and depth provides a clean, flat grinding surface for each grinding cycle. Grinding stones (optionally Al2O3 or SiC) can be changed easily within minutes by unscrewing the center bolt, following which the system will auto-calibrate. The unit is easy to operate with the help of a membrane keyboard, which also displays program parameters. A robust cast-metal housing and an interlocked protective cover with magnetic contacts, which disconnect the grinder as soon as the cover is opened, ensure a maximum of safety.

Its compact bench top design enables the PlanarMet 300 to sit side-by-side with the Buehler EcoMet/AutoMet Grinder-Polisher. The PlanarMet 300 uses the same central force specimen holders as the EcoMet/AutoMet Grinder-Polisher, allowing the user to complete additional preparation steps after planar grinding directly on the polishing system, without transferring to a new holder.

Buehler – ITW Test & Measurement GmbH will be showcasing the new PlanarMet 300 planar grinder at Control 2015, held from May 5th to 8th in Stuttgart/Germany, at its booth 5135 in hall 5.

Buehler – ITW Test & Measurement GmbH, based in Düsseldorf/Germany, has been a leading manufacturer of scientific equipment, supplies and accessories for use in metallography and materials analysis for more than 75 years, and also offers a broad range of hardness testers and hardness testing systems. A close-knit network of branch offices and dealers provides customers with expert support and service around the globe. The central lab located in Düsseldorf/Germany offers assistance with all application-related questions or the development of repeatable specimen preparation processes.
Buehler is part of the Test and Measurement Group of the US based Illinois Tool Works (ITW) group of companies with more than 850 distributed business units in 52 countries worldwide and a staff of approx. 60,000.

Editorial contact and address for voucher copies:

Dr.-Ing. Jörg Wolters, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25,  D-64823 Groß-Umstadt – www.konsens.de

Tel.: +49 (0) 60 78 / 93 63 - 0, Fax: - 20,  E-Mail: mail@konsens.de

Dear editors, please download this Buehler press release including text and ready-to-print image file from: www.konsens.de/buehler.html