Hall 6, Stand E02

ILLIG HSA 50d Automatic Blister Packaging Machine

Focused on Attractive Product Presentation at POS

Heilbronn and Düsseldorf, May 8, 2014. – At this year's Interpack, Düsseldorf, May 8 to 14, ILLIG will present the HSA 50d automatic blister packaging machine for economic production of high-quality packs in different versions for the non-food sector, in small to medium batch sizes. Performance and flexibility of this packaging machine will be demonstrated by the production of blister packs for highlighters. The blister pack consists of a card with brilliant print, possibly upgraded, which is sealed by an accurately fitting transparent blister cap. The whole production sequencing of such a pack can be followed on the exhibited HSA 50d machine, from material feeding through to thermoforming, cutting and filling of the formed blister caps, placing of the printed card and sealing of the pack for the point of sale (POS). Moreover, the machine is equipped with a laser printer for printing the reverse side of the cards. Besides applying universal information, such as QR and bar codes or minimum shelf life dates, packs with different contents can be individually marked, also for traceability. The HSA 50d automatic blister packaging machine features a forming area of max. 500 mm x 300 mm, with a layout possible for up to 12 packs (subject to pack size) and a production speed of up to 20 cycles per minute.

Quick-change devices used by ILLIG in these lines make the HSA 50d highly flexible and very short changeover times are achieved for mold and format changes. Moreover, the standard components of the machine – the waste-free working thermoforming unit as well as the sealing station – can be complemented to form a fully automated packaging line by employing different optional extras adjusted to the corresponding packaging task: A feeding device for the parts to be packed, a card loading device, a pack turning device in the discharge unit. The modular line is completely interlinked with Profibus interfaces, relocation or retrofitting of additional units is possible at every position. The interaction of machine, mold and additional units is the basic requirement for smooth production if such complex packaging systems are employed with a high degree of automation. The thermoforming unit of the automatic blister packaging machine features a high indexing accuracy thanks to the transport's servo drive which has a very positive effect on the cutting accuracy of the blister caps. A reliable blister transfer allows uniform and jerk-free motions so blisters can be placed precisely in the sealing pallets. The universal, modular HSA system allows flexible production of various packs which meet all requirements with respect to a modern blister pack: Transport protection of products combined with authenticity protection and attractive presentation with high recognition value at the POS at the same time.

ILLIG is a global leading supplier of high-performance production lines and molds for thermoforming plastic materials as well as of solutions for the packaging industry. The company's product and services portfolio comprises the development, design, fabrication, installation and start-up of complex manufacturing lines and individual components. With branch establishments and agencies in over 80 countries, ILLIG is locally present in all markets around the globe. For more than 65 years, this owner-managed enterprise has been serving its worldwide clientele as a reliable partner in cost-efficient thermoplastic molding of sophisticated precision parts backed by innovative technology of unsurpassed quality and a comprehensive worldwide after-sales support.

■■■

Further information:

Wolfgang Konrad, Director Public Relations

ILLIG Maschinenbau GmbH & Co. KG, Robert-Bosch-Straße 10, D-74081 Heilbronn

Phone: +49 (0) 71 31 / 5 05 – 2 36, Fax: - 12 36,  E-Mail: wolfgang.konrad@illig.de

Editorial contact and voucher copies:

Dr. Georg Krassowski, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25,  D-64823 Groß-Umstadt – www.konsens.de

Phone: +49 (0) 60 78 / 93 63 - 0,  Fax: - 20,  E-Mail: georg.krassowski@konsens.de

Dear colleagues,

ILLIG press releases, including text (German and English) and photos in
	printable resolution, are available for download at:

www.konsens.de/illig.html

HSA 50d automatic blister packaging machine presented by ILLIG at Interpack for versatile, flexible and economic production of attractive blister packs for non-food articles.

Picture: ILLIG