Hall 11, Stand C54

ILLIG at Interpack 2011

ILLIG's new FSL 48 – redefining the standards in hygienic decorative packaging of dairy products

Heilbronn and Düsseldorf, 12 Mai 2011. – At this year's Interpack in Düsseldorf, one key focus of ILLIG's trade show presentation will be on the new FSL 48 forming, filling and sealing machine. Designed with the demands of the foodstuffs and, specifically, dairy product industries in mind, the unit delivers single-serve packaging containers with high-grade photo quality decorations made by in-mold labeling (IML) directly in one operating step with the thermoforming process. Following hygienic filling, the containers are then sealed to obtain a finished retail-packaged article. What is more, ILLIG is premiering an all-new “experience presentation” approach for its exhibits this time – a “virtual machine presentation” using 3D visual rendering techniques that provide a detailed view of the relevant machine assemblies and the line's intermeshing process sequences leading up to the final product. Traditional machine displays at trade fair booths had given visitors all but no chance of gaining such insights. In addition, the integrated processing lines increasingly characteristic of modern-day manufacturing can no longer be conveniently exhibited on the trade show floor for space reasons.

The new FSL 48 – hygienic & decorative filling and packaging of dairy products

The hygiene levels supported by the new FSL 48 range from thermoforming IML-decorated cups with sterile air through a configuration with an all-enclosed filling section to the optional sterilization of lid foil by UV irradiation. Moreover, the machine's newly developed multi-track filling unit is designed to provide CIP (cleaning in place) and SIP (sterilization in place), making it generally suitable for aseptic filling. Thus, the FSL 48 delivers filling and packaging capabilities which reliably conform to diverse standards up to VDMA Hygiene Class IV for hygienic filling equipment. Thanks to the multi-track filling unit, cups can be filled with up to eight different product varieties at the same time. The new FSL 48 can process all customary sheet stock suitable for FFS lines, e.g., PS, PP, multilayer materials (e.g., PS/EVOH/PE), APET, and even stock made of PLA (polylactide) organic polymers. The same applies to the heat-sealable lid material.

The format surface area of 480 mm x 320 mm (or up to 350 mm in the case of non-decorated articles) makes it possible to accommodate the output of one complete cycle – e.g., 12 standard curd cheese packs – in a carton compatible with the Euro pallet module following sealing and separation of the cups from the web. This format size is adaptable to obtain single or dual cups, or 4- or 6-cup trays. The machine's controlled, exclusively servomotor-driven movements result in a very smooth operation, so that even highly liquid products can be filled into single-serve packs at rates exceeding 30 cycles/minute without product overspilling onto the sealing rim.

Apart from the machine version with integrated IML unit (FSL 48 model), the basic machine is also available in its FS 48 standard form for thermoforming, filling and sealing single-serve packs or other non-decorated foodstuff containers. Any configuration of this FFS machine – whether FS 48 or FSL 48 – can be combined with a carton packer matching its output capacity. The packer, which is also servomotor-driven, features an automatic carton erector and can handle any kind of carton, from trays to open-top to wraparound types.

IML: Brilliant custom decoration of a broad diversity of cup geometries

The IML unit developed for the FSL 48 uses printed pre-cut labels supplied from a storage magazine. These labels are placed in the mold cavity and become integral with the cup wall in the subsequent thermoforming cycle. Since the IML process does not require vertical container walls, this decorating method provides the additional benefit of supporting a broad diversity of cup shapes for improved visual impact on the supermarket shelf. Indeed, IML opens up a broad range of cup decorating options – from one-sided, two-sided or three-sided (e.g., U-shaped) to four- or even five-sided (including a bottom decoration, e.g., with an integral bar code) designs – to combine high visual appeal with superior functionality. Depending on the cup material, the technology supports matching PP, PS or paper labels. The IML unit is integrated directly into the molding station and requires no more floorspace than a conventional banding unit.

Another advantage of the IML technology employed consists in the fact that each mold cavity can accommodate a differently printed label. Such versatility is helpful in filling and packing product families, which is basically made possible by the multi-track filler configuration. Product changes too are quick and easy to implement with this technology.

Inserting the labels into the mold adds an additional operating step to the thermoforming workflow. In the interests of attaining maximum productivity (i.e., high cycle rates) despite this requirement, the label is inserted concurrently with the ongoing molding step outside the closed mold. To this end, the lower part of the mold is in the shape of a fourfold cube which rotates through 90 deg. in every cycle. Each printed label is inserted and fixed in the cavity with the lower mold part awaiting its next 90-deg. turn into the molding position. At the rate of 30 cycles/minute that can thus be achieved, and with the useful sheet stock area sized to yield, e.g., 12 standard curd cheese packs, the machine will thus deliver 21,600 single-serve packs per hour – hygienically filled and sealed into a custom-designed container of high decorative appeal for sustainable presentation on the POS shelf.

ILLIG is a global leading supplier of high-performance equipment and tooling for thermoforming plastic materials as well as of solutions for the packaging industry. The company's product and services portfolio comprises the development, design, fabrication, installation and start-up of complex manufacturing lines and individual components. With wholly owned branch establishments and agencies in over 80 countries, ILLIG is locally present in all markets around the globe. For more than 60 years, this owner-managed enterprise has been serving its worldwide clientele as a reliable partner in cost-efficient thermoplastic molding of sophisticated precision parts backed by innovative technology of unsurpassed quality and a comprehensive worldwide after-sales support.

■■■

Further information:

Wolfgang Konrad, Head of Corporate Communications and PR

ILLIG Maschinenbau GmbH & Co. KG, Robert-Bosch-Str. 10, D-74081 Heilbronn / Germany

Phone: +49 (0) 71 31 / 5 05– 2 36, Fax: - 12 36,  E-mail: wolfgang.konrad@illig.de

Editorial contact and voucher copies:

Dr. Georg Krassowski, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Str. 25,  D-64823 Groß-Umstadt / Germany – www.konsens.de

Phone.: +49 (0) 60 78 / 93 63 - 0,  Fax: - 20,  E-mail: georg.krassowski@konsens.de

Dear Colleagues,

ILLIG press releases, comprising the text (in German and English) and images 
      in print-quality resolution, are available for download at:

www.konsens.de/illig.html

The new forming, filling and sealing machine FSL 48 is cut out for the task of hygienic filling and packaging of dairy products – including, e.g., product families of differently flavored varieties – in thermoformed IML-decorated cups.

The IML unit of the FSL 48 machine withdraws labels printed in brilliant photo quality from a storage unit and transfers them into a mold cavity. Diverse cup geometries are supported. Even the bottom of the cup may be used – e.g., to apply a large and easy-to-read bar code without interfering with product design.

Photos: ILLIG