PRESS RELEASE 	Contact: 	Simone Hebel 
		Marcom Specialist

Instron Deutschland GmbH

Tel.: +49 (0) 6157 4029 614

simone_hebel@instron.com

New Drop Weight Impact Tester Covers Broad Spectrum of Applications

|  | The new Instron CEAST 9340 Drop Weight Tester delivers impact energies from 0.30 J to 405 J and is suitable for a broad range of impact applications, including tensile impact and penetration tests on plates and films, testing of pipes and small components, and Izod and Charpy testing. Image: Instron Dear editors, Please download Instron press releases including text and ready-to-print image file from: www.konsens.de/instron.html |
| --- | --- |

Pfungstadt/Germany, January 2011 – Instron’s new CEAST 9340 Drop Weight Tester is a floor-standing, compact impact test instrument designed to deliver impact energies from 0.30 J to 405 J (with falling weights ranging from 1.0 kg to 37.5 kg). With a full range of accessories, the system is suitable for variety of applications, including tensile impact and penetration testing of plates and films, testing of pipes and small components, and testing to Izod and Charpy. The standard model includes a conveniently mounted machine controller for operation of the test system. In addition, the system can be equipped with the CEAST Visual IMPACT Software.

Amongst the special features of the CEAST 9340 Drop Weight Tester are a 490 mm wide ( 450 mm deep ( 565 mm high, fully enclosed and interlocked test area protecting the operator from specimen fragments, a motorized crosshead positioning system, changeable tups and inserts, a full set of weights graduated in increments of 0.5 kg and the capability of adding a temperature chamber. For instrumented impact testing, the system can be extended with the CEAST Data Acquisition Systems DAS Junior, DAS 16000 or DAS 64K. The CEAST 9340 Drop Weight Tester is a member of the CEAST 9300 family of impact testers designed for impact energies from 0.25 J to 20.4 J in the case of the Model 9310 and from 0.59 J to 1,800 J in the case of the Model 9350.

About Instron

Instron is a globally leading manufacturer of test equipment for the material and structural testing markets. A global company providing single-source convenience, Instron manufactures and services products used to test the mechanical properties and performances of various materials, components and structures in a wide array of environments. Instron systems evaluate materials ranging from the most fragile filament to advanced high-strength alloys. With the combined experience of CEAST in designing plastic testing systems, Instron enhances materials testing offerings, providing customers with comprehensive solutions for all their research, quality and service-life testing requirements.

Additionally, Instron offers a broad range of service capabilities, including assistance with laboratory

management, calibration expertise and customer training.

– – – – –

Editorial contact and voucher copies:

Dr.-Ing. Jörg Wolters, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25,  D-64823 Groß-Umstadt – www.konsens.de

Tel.: +49 (0) 60 78 / 93 63 - 0,  Fax: - 20,  E-Mail: mail@konsens.de