| Material preparation – energy-efficient, flexible and with improved price/performance ratio New SOMOS® T/TF eco dryer now available as complete series The new SOMOS® T/TF eco dryer from MANN+HUMMEL ProTec presented at K 2007 is now available as a complete series in five different sizes. These flexible dry-air dryers combine energy efficiency with a particularly good price/performance ratio. Bensheim, 14 October 2008 – The new mobile SOMOS® T/TF eco dryers consist of a dry-air generator and an insulated stainless-steel drying hopper. They are available in the T-version or as a TF-version with integrated conveyor for automatic processing-machine feeding. With hopper sizes of 30 l to 300 l usable volume, graded in six sizes and an appropriate dry-air throughput of 10 m³/h to 100 m³/h, the material quantity adjusted to the throughput of the processing machine can be prepared flexibly near the machine. To ensure economical energy consumption, the new T/TF dryer generation is equipped with the energy-saving technologies known from SOMOS® dryers: automatic adjustment of the dry-air quantity to the material throughput (ALAV) and the Super-SOMOS® function for adjusting the regeneration frequency of the desiccant to the actually adsorbed moisture quantity. The dryer series is tailored to small quantity requirements of approx. 3 kg/h to material throughputs of 80 to 100 kg/h. Drying temperatures of 60 to 140 °C with a dew point temperature of -35 °C are covered. Thanks to the easy retrofitting of a microfilter, the dryers of the SOMOS® T/TF eco series can also be used in clean-room production. An easy-to-operate microprocessor control unit monitors, regulates and documents all dryer functions. Dry air is constantly applied to the conveyor of the TF dryer version in order to prevent the remoistening of the dried granulate. To support the process, small material quantities ensure that dry granulate with approximately constant material temperature is always available to the processing machine. The hopper geometry, optimised to the material flow, leads to an even, narrow dwell time distribution of the material being dried, and thus to consistency in the quality of the dried material. These inexpensive and energy-efficient mobile dry-air dryers are thus particularly suitable for processing small to medium material throughputs without a central drying system or in which frequent material changes are necessary. Rapid conversion – easy operation The new round and insulated stainless-steel drying hoppers are free of dead space and can be simply and rapidly cleaned for a material change. The desiccant bowl can also be replaced as a complete component in a few simple steps. Such design features ensure that the maintenance costs for the SOMOS® T/TF eco series remain at an overall low level. The standard equipment of the user-friendly microprocessor control unit also includes, in addition to an automatic throughput-dependent economy setting, a weekly time switch and a maintenance display for desiccant and filter. There are also many safety features integrated in the control unit. The function of the check flaps, fan, heating rods and compressed air connection, and desiccant status and optimisation of the desiccant regeneration, are continually monitored and regulated. All functions, including logs and data-recording software, can be recorded via the RS 232 interface for purposes of documentation. (approx. 3.400 characters) About MANN+HUMMEL MANN+HUMMEL is a development partner and series supplier of the international automobile and mechanical engineering industries. In 2007, 11,500 employees at 41 locations around the world generated a turnover of 1.75 billion Euro. The product range of the corporation includes air filter systems, intake systems, fluid filter systems, cabin filters and plastic cylinder head covers with a high degree of integration for the automobile industry, as well as filter elements for the maintenance and repair of motor-vehicles. For the mechanical engineering, process technology and industrial manufacturing sectors, the product range includes industrial filters, a programme for the reduction of soot emissions in diesel engines, filter systems, as well as equipment for material handling. MANN+HUMMEL ProTec GmbH develops, plans and sells solutions for material preparation and handling in the plastics-processing industry, ranging from individual devices to complete systems. Further information on MANN+HUMMEL ProTec is available at: www.mh-protec.com Dear colleagues, Press releases of MANN+HUMMEL ProTec with text and photos in printable resolution you will find as a download at www.konsens.de/mh-protec.html Please send voucher copies to: Konsens PR GmbH & Co. KG, Dr. Georg Krassowski Hans-Kudlich-Str. 25, D-64823 Groß-Umstadt, Germany The new energy-efficient and inexpensive dryers of the SOMOS® T/TF eco series (the photo shows the TF 70 eco with integrated mounted conveyor) are compact, well equipped and versatile – especially when frequent material changes are necessary or small to medium throughputs are processed without a central drying system. Photo: MANN+HUMMEL ProTec | MANN+HUMMEL ProTec GmbH Stubenwald-Allee 9 64625 Bensheim, Germany Press contact: Grit Schmidt Phone: +49 (0) 62 51 7 70 61-150 Fax: +49 (0) 62 51 7 70 61-81-150 e-mail: presse@mh-protec.com Internet: www.mh-protec.com MANN+HUMMEL ProTec at FAKUMA 2008 14 – 18 October 2008 Friedrichshafen Hall B3, Stand 3120 MANN+HUMMEL ProTec GmbH Stubenwald-Allee 9 64625 Bensheim, Germany Press contact: Grit Schmidt Phone: +49 (0) 62 51 7 70 61-150 Fax: +49 (0) 62 51 7 70 61-81-150 e-mail: presse@mh-protec.com Internet: www.mh-protec.com MANN+HUMMEL ProTec GmbH Stubenwald-Allee 9 64625 Bensheim, Germany Press contact: Grit Schmidt Phone: +49 (0) 62 51 7 70 61-150 Fax: +49 (0) 62 51 7 70 61-81-150 e-mail: presse@mh-protec.com Internet: www.mh-protec.com MANN+HUMMEL ProTec GmbH Stubenwald-Allee 9 64625 Bensheim, Germany Press contact: Grit Schmidt Phone: +49 (0) 62 51 7 70 61-150 Fax: +49 (0) 62 51 7 70 61-81-150 e-mail: presse@mh-protec.com Internet: www.mh-protec.com |
| --- | --- |