Hall B3, Booth 3119

ProTec Polymer Processing at FAKUMA 2012

SOMOS® BB150: A new, powerful gravimetric batch dosing system

Bensheim and Friedrichshafen/Germany, October 16, 2012. – The new gravimetric batch dosing system SOMOS® BB150 displayed at Fakuma is suitable for supplying injection molding machines as well as for extruders operating in overfeeding mode with multi-component mixtures. It is designed for a total of four free-flowing materials and a throughput of up to 150 kg/h. The system is mounted onto a frame near the machine and can be equipped with SOMOS® suction conveyors for automatic filling of the material tank. The new batch dosing system SOMOS® BB150 offers high dosing precision at an attractive price-performance ratio. Ease of use is ensured by the MH45 touchscreen controller equipped with a graphical user interface specially tailored to the range of tasks performed by a batch dosing machine.

The individual components are dosed in sequence into a weighing chamber according to the recipe and the entire batch then homogeneously mixed by a four-blade mixer in a mixing chamber below. The weighing chamber has a volume of 3 l, the mixing chamber a volume of 9 l. The discharge from the material supply, weighing and mixing chambers is equipped with pneumatically operated slide gate systems. To regulate the material flow into the weighing chamber, a reduction ring can be fitted to the discharge from the material supply hopper to reduce its diameter. In addition, the cylinder stroke for opening the slide can be reduced with the aid of set screws. In this way, the SOMOS® BB150 batch dosing system enables extremely cost-effective gravimetric dosing of mixing proportions of even less than 1 % using slide gate systems, achieving precisions of ± 1 % of the dosing weight of the respective component. Quick releases and spacious entry to the material hoppers and weighing area as well as removable mixer components enable materials can be changed very easily and quickly.

An intuitive and powerful controller with a 6" color touchscreen is included as standard in this high-quality design. The local memory in the network-enabled controller can also store and provide direct access to as many as 100 recipes. A USB interface fitted as standard allows users to export recipes and data or import additional, externally stored recipes. The controller for the dosing system can also be used simultaneously to control conveyors: A conveyor for feeding the supply hopper can be allocated to each dosing component. To prevent the system operator from making unauthorized changes to the controller, the MH45 features two operating levels, whereby access to the administrator level is password-protected.

ProTec Polymer Processing GmbH with headquarters in Bensheim bundles the renowned brands SOMOS® and OHL: Machines and entire system solutions for efficient material handling in all plastic treatment processes currently in use, machines for the post-condensation of solid plastic matter as well as turn-key machines for bottle-to-bottle recycling of PET. ProTec Polymer Processing is a member of the Schoeller Plast Industries Group of companies with manufacturing locations in Germany, Denmark and Brazil. The company's integration into the global sales and service network of the Schoeller Group (www.schoeller.org) offers the optimum infrastructure for comprehensive on-site customer service.

■■■

# Further information:

Grit Feistkorn, Manager Marketing

ProTec Polymer Processing GmbH, Bensheim Headquarters, Stubenwald-Allee 9, D-64625 Bensheim

Phone: +49 (0) 6251 77061-150, Fax: - 81 150,  E-mail: grit.feistkorn@sp-protec.com

# Editorial contact and sample copies:

Dr. Georg Krassowski, Konsens PR GmbH & Co. KG,

Hans-Kudlich-Straße 25, D-64823 Groß-Umstadt – www.konsens.de

Phone: +49 (0) 60 78 / 93 63 - 0,  Fax: - 20,  E-mail: georg.krassowski@konsens.de

Dear Colleagues,

Press releases from ProTec Polymer Processing containing text (German and English)
	as well as images in print-ready resolution are available for downloading at:

www.konsens.de/protec.html

The new gravimetric batch dosing system SOMOS® BB150 is designed for up to four free-flowing materials and a throughput of up to 150 kg/h.

Picture: ProTec Polymer Processing